## Slide 1: Interpreting Hemodynamic Data. Pressures Flow and Resistance Estimations
S.RADHAKRISHNAN
FORTIS ESCORTS HEART INSTITUTE AND RESEARCH CENTRE, NEW DELHI

## Slide 2
PROF R TANDON 1928- 2014. FRIEND AND MENTOR

## Slide 3: Questions: Before, During and After Catheterization
Why are we catheterizing this patient with congenital heart disease?
What specific information is being sought?
What factors can influence interpretation of the information?

## Slide 4: Why are we Catheterizing this patient with Congenital Heart Disease?
So that we can take a better informed decision on management

## Slide 5: Why are we catheterizing this patient with Congenital Heart Disease?
What are the indications for performing Cardiac Catheterization?
Anatomic Definition (Angiography)
Physiologic Quantification (Hemodynamics)
Pressure
  Flows
  Resistances

## Slide 6: PRESSURES
Catheter tipped manometers are still considered gold standard. Rarely available in clinical setting
Fluid filled tubings and catheter are prone to errors
Great pains to be taken to minimize errors
  Level of transducer in relation to chest
  Constant check on calibration and zeroing during procedure
  Recognize under and over damping of pressures and correct

## Slide 7: Why are we catheterizing this patient with Congenital Heart Disease?
Flows and Resistances:
Operability in borderline situations
Before single ventricle palliation (Glenn / Fontan)

## Slide 8: When Do We Need to Catheterize Patients With Left to Right Shunts?
Clear clinical /noninvasive evidence of a large left – right shunt. Typically younger patients
Operable
Inoperable: Eisenmenger physiology
Clear evidence of shunt reversal resulting from high PVR. Typically older patients
Borderline situation: PVR elevated by clinical/non-invasive assessment. Degree of elevation of PVR (and therefore operability) uncertain.

## Slide 10
LV
RV
LA
LV
RA
RV
Clearly Operable: Cath not required

## Slide 11: When Do We Need to Catheterize Patients With VSD, PDA?
Clear clinical /noninvasive evidence of a large left – right shunt
Operable
Clear evidence of shunt reversal resulting from high PVR.
Failure to thrive,  precordial activity, mid diastolic murmur at apex,
Cardiac enlargement, pulmonary blood flow
Q in lateral leads on ECG, good LV forces
LA/LV enlargement, exclusively L-R flows across the defect
Inoperable
Cyanosis, desaturation at rest (<93%) or on walking, quiet precordium, no MDM
Normal heart size, peripheral pruning
No Q in lateral leads, predominant RV forces
No LA LV enlargement, significant R-L flows across the defect
Borderline clinical non-invasive data: uncertain operability

## Slide 12
26 year old
Blue
Single loud S2

## Slide 13
Clearly Inoperable: Cath not required? Sometimes performed before “labeling as inoperable”
RV
LV
RA
LA

## Slide 14
14-year-old boy
19.7 Kg
Pink (95%)
Closely split S2
Loud P2
No apical MDM,
ECG RVH, no Q in lat leads

## Slide 15
LA
LV
RA
RV

## Slide 16
RV
Ao
LA
LV
Ao
PA
PDA
Operability Uncertain :
Cardiac cath recommended

## Slide 17: Questions: Before, During and After Catheterization
Why are we catheterizing this patient with congenital heart disease?
What specific information is being sought?
What factors can influence interpretation of the information?

## Slide 18: What Specific Information is being sought?
How much is the shunt?
  - Ratio of pulmonary to systemic blood flow (Qp: Qs ratio)
PVR / PVRI; PVR/SVR ratio?
Ventricular end diastolic pressure (for Single Ventricle physiology)

## Slide 19: Flow Calculations
Applying Fick’s Principle
Oxygen Consumption
O2 content 1
O2 Content 2
Flow =

## Slide 20: Flow Measurements: O2 Content
O2 Content (ml of O2 per 100 ml of blood)
Hb (gm/100 ml of blood) X 1.36 X fractional saturation of blood
  +
Dissolved Oxygen in plasma

## Slide 21: Dissolved O2
0.003 ml of O2 is dissolved in 100 ml plasma for every torr (mm Hg) of Oxygen tension
Should be taken into consideration whenever PO2 exceeds 100 mm Hg after O2 is administered

## Slide 22: Oxygen Saturation Measurements
Direct saturation measurements and not ABGs
Saturations should be measured in the lab
Spectrophotometer (measures absorption of transmitted light at a given wavelength)

## Slide 23
HEAMOXYMETER

## Slide 24: Flows
Pulmonary blood flow
Oxygen consumption
PVO2 content
PA O2 Content
Systemic blood flow (cardiac output)
Oxygen consumption
Arterial O2 content
Mixed V O2 Content

## Slide 25: Flows
Pulmonary blood flow
Oxygen consumption
Systemic blood flow (cardiac output)
Oxygen consumption
(Ao sat – MV sat) (Hb conc) (1.36) (10)
(PV sat – PA sat) (Hb conc) (1.36) (10)

## Slide 26: Shunt Ratio (Qp/Qs)
Only O2 saturations are needed
Aortic sat – Mixed Venous sat
Pulmonary Venous sat – PA sat

## Slide 27: Shunt Calculations in admixture lesions
Effective Systemic (QeS) or Pulmonary blood flow (QeP)
Oxygen Consumption
(PV sat – MV sat) (Hb conc) (1.36) (10)
L-R Shunt = Qp – Qep; R-L shunt = Qs - Qes

## Slide 28: Flow Calculations: Sources of Error
Sampling for O2 saturation estimation
Streaming
Partial wedging

## Slide 29: O2 Saturation Errors
Getting samples in different physiologic states
Diluted samples
Air bubble in syringe
Delay in sending samples
Machine calibration
Extrapolating from ABG
Failure to account for dissolved O2
Carboxyhemoglobin

## Slide 30: O2 Saturation Errors
Non representative sampling
Pulmonary vein
Right atrium
IVC
Aorta in presence of
PDA with R-L flow

## Slide 31: Mixed Venous Saturation
In absence of L - R shunt: PA
In presence of L - R shunt:
  ?SVC
  ? Flamm Formula (3 SVC +1IVC / 4)
Anesthesia

## Slide 32: Oxygen Consumption
Measured:
Douglas bag, Spirometer
Flow through devices (Waters; Sensormedics)

## Slide 33: Oxygen Consumption

## Slide 34: Oxygen Consumption
Assumed:
Older Patients: Tables, Formulae of LaFarge and Miettinen
  HR, age, sex, wide standard deviation
Infants: Crude approximations
  2-5 Kg: 10-14 mlO2/Kg
  5-8 Kg: 7-11 mlO2/Kg
  ** Assumed oxygen consumption on O2 is NOT RECOMMENED

## Slide 35: Flow Calculations: Limitations
Errors in oxymetry
Assumptions:
  O2 Consumption
  PV O2 saturation
High flows (limits use of Fick’s method)

## Slide 36: Sampling Sequence
1
?2
3
1

## Slide 37: What is a Significant Step-up? Shunt detection by oxymetry
Chamber Sampled | Minimum Difference | Multiple Samples
SVC-RA | 8.7% | 7%
RA-RV | 5.2% | 4%
RV -PA | 5.6% | 4%

## Slide 38: Criteria for step-up

## Slide 39: PVR Estimation
Pulmonary artery mean pressure
Pulmonary venous mean pressure
Trans-pulmonary gradient
PVR =
Pulmonary blood flow
Oxygen consumption
PVO2 content
PA O2 Content

## Slide 40: Determinants of Pulmonary Vascular Resistance (PVR)
 PVR |  PVR
Hypoxia | Oxygen
Hypercarbia/acidosis | Hypocarbia/Alkalosis
Hyperinflation | Normal FRC
Atelectasis | Nitric Oxide
High hematocrit | Low hematocrit

## Slide 41: Left to Right Shunts: Conditions that increase PVR
Lung infections
Hypoventilation
  Upper airway obstruction
  Skeletal deformities of chest wall
  Deep sedation
Chronic lung disease
Underdeveloped lungs
Pulmonary venous obstruction

## Slide 42: Heart Lung Interactions: L - R Shunts with Hypoventilation
Infants with Trisomy 21
VSD, Common AV canal and PDA
Hypoventilation from upper airway obstruction is very common
Resting elevation of PVR because of low PO2 and high PCO2
Problem exaggerated by sedation (during cath and echo)

## Slide 43: Heart Lung Interactions: L-R Shunts with Hypoventilation
Trisomy 21
Pierre-Robin Syndrome
Neurogenic hypoventilation
Skeletal deformities (Kyphoscoliosis)
Assessment of operability and decision making can be very difficult

## Slide 44: Special maneuvers in Cath lab
PDA occlusion to assess operability
Temporary occlusion of fenestrated Fontan to assess suitability of closure
Temporary occlusion of venous collaterals (pop off channels) post Glenn operation

## Slide 47
72
86
97
98
80
8
40
16
80
Qp/Qs =
97-72 / 98-86 = 25/12
~2:1
Cardiac Index: 3.2l/min/m2
Qp = 6.4 l/min/m2
PVRI =
40-16/6.4; 24/6.4 = 3.75 wood units (mmHg/l.min.m2)

## Slide 48
72
86
97
98
80
8
40
16
80

## Slide 49: PVR assessment in the presence of asymmetric pulmonary blood flows
Rt
Lt
1/PVR = 1/pvr(rt) +1/pvr(lt)

## Slide 50: Some rules in interpreting hemodynamic data
Pressures: Normal/high or low
Gradients if any
Trans-pulmonary gradient
Diagnostic possibilities (keep this for the end)

## Slide 51: Some rules in interpreting hemodynamic data
Background Knowledge -
All normal values
Pressure recordings, principles and sources of error
Principles of flow and resistance calculations, sources of error
Principles of valve area calculations, sources of error

## Slide 52: Some rules in interpreting hemodynamic data
Look at one parameter at a time:
Oxygen saturations followed by pressures
SVC sats: Normal High or low
Is there a significant step-up downstream at all levels
Is there a step-down in the sats
Quick calculation of Qp/Qs

## Slide 53: SUMMARY
Cardiac Cath in patients for CHD is a cumbersome process
Inherent errors at all steps
Every effort to minimize errors
Rapid changes in hemodynamics during procedure should be recognized and efforts made to correct it
Patient should be in as near physiological state as possible (chest infection, fever)

## Slide 54: SUMMARY
Need for angiography minimized with availability of alternate modes of imaging
Calculations modules available in computer but important to allow resident to practice manual calculations
Need to further develop techniques like MRI for flow calculation

## Slide 55: Hemodynamic Tracings
Rhythm on ECG
Scale and paper speed
Chamber: Atrial-venous / ventricular / arterial
Identify waves (in atrial tracings), which is taller
Numbers, normal or elevated
Quality (only if abnormal, under-damped with overshoot, over-damped)
Characteristics of the waves
Respiratory variation, report end expiratory pressure
Effect of ectopic if any
Interpretation
Diagnostic possibilities, there may be more than one!

## Slide 56
120
160
LV and aortic pressure tracings
What is the diagnosis?

## Slide 57
RV to RA pull back tracing

## Slide 60
AO
PA
Balloon Occlusion
Balloon deflation

## Slide 61
Pre Proc

## Slide 62
Post Proc

## Slide 64
What sign is shown?
Notes: Before pericardiocentesis.

## Slide 65
Notes: After…